## Slide 1: DSD FINAL PRESENTATION
RICV G2
電機三 蔡易霖 趙彥安 劉凡

## Slide 2: Branch prediction

## Slide 3: Two level adaptive predictor
Bn-2 | Bn-1
0 | 0
00 | Strongly taken
01 | Stongly not taken
10 | Weakly taken
11 | Weakly not taken
Branch history
Branch history table

## Slide 4: Accuracy of each predictors
2 level adaptive predictor outperforms its counterparts!
Interleave in BrPred: 10..10..10-> history register cannot store 1 when IF stage need to predict 0
Chart: Accuracy of has hazard
| always taken | always not taken | 1 bit | 2 bit | 2 level
 | 52 | 48 | 16 | 45 | 91
Chart: Accuracy of branch prediction
| always taken | always not taken | 1 bit | 2 bit | 2 level
 | 65 | 35 | 50 | 67 | 70

## Slide 5: Disadvantage
Much more area!
N bits history -> Need 2N saturating counter

## Slide 6: Local branch predictor
bne 11
beq 01
00 | Strongly taken
01 | Weakly taken
10 | Weakly not taken
11 | Stongly not taken
00 | Weakly taken
01 | Stongly taken
10 | Stongly not taken
11 | Weakly taken
bne
Respective branch history

## Slide 7: Accuracy
Chart: Accracy of has hazard
| always taken | always not taken | 1 bit | 2 bit | 2 level | local
 | 52 | 48 | 16 | 45 | 91 | 94
Chart: Accuracy of branch prediction
| always taken | always not taken | 1 bit | 2 bit | 2 level | local
 | 65 | 35 | 50 | 67 | 70 | 97

## Slide 8: Disadvantage
Area: i branch instructions, j bits history for each instruction
Need i*2j saturating counters!

## Slide 9: Compression
TOP
I_mem_rdata
[25:24]=2’b11
(32 bit)
PC+4
BOTTOM
16
PC+2
TOP 32
PC+2
I_mem_rdata
[9:8]=2’b11
32+32
I_mem_rdata
[9:8]=2’b11
32+32
I_mem_rdata
[9:8]!=2’b11
32+16
I_mem_rdata
[9:8]!=2’b11&&
I_mem_rdata
[25:24]!=2’b11
16+16

## Slide 10: Advantage of compression
Reduce miss rate
Require less cache size
Consume less energy

## Slide 11: Miss rate and cache size
Chart: Miss rate
| compression | decompression
 | 2.3 | 6.3
Ref:https://people.eecs.berkeley.edu/~krste/papers/waterman-ms.pdf

## Slide 12: Improve energy efficiency

## Slide 13: L2 Cache
Best Format:
  L1 cache: write through
  L2 cache: write back
Our Format:
  L1 cache: write back
  L2 cache: write through

## Slide 14: Our Comparison
Separate Cache:
  Direct map memory 64/128 words
Unified Cache:
  Direct map memory 128/256 words
  An extra bit to classify I or D

## Slide 15
Area & execution time under same cycle time
Chart: L2Cache Execution Time
| 256_unified | 128_unified | 128_dm | 64_dm
 | 461461 | 467599 | 461600 | 468496
Chart: L2Cache Area
| 256_unified | 128_unified | 128_dm | 64_dm
 | 905408 | 598398 | 764786 | 532583

## Slide 16: A*T Value
Chart: L2Cache A*T Value
| 256_unified | 128_unified | 128_dm | 64_dm
 | 41781048 | 27981030 | 35302521 | 24951300

## Slide 17: L2 Cache Miss Rate
L2 Cache | Miss Rate
256_unified | 5.8%
128_unified | 7.6%
128_dm | 6.6%
64_dm | 8.9%
Better Miss Rate in our design:
Unified > Direct map memory !